## Slide 1: Early Results From ADMX-G2 Axion Dark Matter Search
HEP Seminar at U. Chicago
February 11, 2019
Andrew Sonnenschein
Fermilab

## Slide 2: Axions-- Motivation
Protons and neutrons have a charged substructure (quarks)
Naïve expectation: they should have electric dipole moment of order 10-16 e-m ?

## Slide 3: Electric Dipole Moments Violate CP (or T) Symmetry
Small electric dipole moment of neutron could be explained by approximate CP symmetry of strong interaction.
But the strong interaction Lagrangian appears to have CP- violating terms that don’t need to be small.

## Slide 4: Peccei Quinn Solution to Strong CP Problem
QCD Lagrangian appears to violate CP due to GG term.
Introduce a new field  coupled to GG with a spontaneously broken symmetry.
To minimize vacuum energy, radial part of  takes on a vacuum expectation value (VEV).
CP violating term in QCD Lagrangian is cancelled out by the VEV of .
 can still move in the axial direction– the axion!
CP violating term
0 in vacuum state

## Slide 5: fA : One Parameter Controls Everything
fA is the “axion decay constant”, an unknown energy scale in the theory.
Determines axion mass and all couplings
fA Originally identified with the electroweak symmetry breaking scale by Peccei and Quinn (~100 GeV), predicting axion mass to be ~ 100 keV.
Coupling to electromagnetic field
Coupling to gluon field
Coupling to fermions

## Slide 6: Predictions Vs. Previous Experiment Constraints
ADMX
(2013)
Yale
Astrophysical bounds
Rochester Brookhaven
Fermilab
U Florida (1990s)
HAYSTAC
Classical “post inflation” axion window: fine tuning not required for axions to make up 100% of observed dark matter

## Slide 7: WIMPs Vs. Axions
WIMPs
  Dramatic progress in attempted WIMP detection over last decade- many models previously considered promising are now excluded.
  Direct searches will become background limited by neutrinos over next 10 years.
Axions
  Previous experiments not sensitive enough to test most important models.
  Emerging techniques likely to reach required sensitivity.

## Slide 8: Diversity of Techniques
“Light Shining Through Walls” (ALPS)
NMR (ARIADNE, CASPER)
Dielectric Radiators (MADMAX, ORPHEUS)
Resonant Cavity (ADMX, HAYSTAC, CAPP)
LC Circuit (DMRADIO, ABRACADABRA)
Photo detector
axion
magnet
Sun
Solar Axions (CAST, IAXO)

## Slide 9: Maxwell’s Equations with an Axion
Irastorza & Redondo 2006
The field is a classical field representing axion dark matter density, oscillating with a frequency corresponding to the axion mass ().
In a background magnetic field, axion is responsible for a new source term which resembles an oscillating electric current
Fictitious electric current
gagg
a



## Slide 10
Magnetic Field (e.g. from a solenoid)
Magnet

## Slide 11
Oscillating Fictitious Current Produced by Axions in Magnetic Field
Magnet

## Slide 12
Magnetic Field Response to Axion Current
Magnet
The current sources a magnetic field.

## Slide 13
Electric Field Response to Oscillating Magnetic Field
Magnet
Small electric response field appears parallel to imposed magnetic field.
Electric and magnetic field amplitudes proportional to ga

## Slide 14
Sikivie Axion Haloscope Detector (ADMX and others)
Magnet
Put a metal cavity (box) in the magnet bore.
Static B field will permeate the (non superconducting) cavity.
Tune the cavity to resonate at axion frequency .
See Pierre Sikivie, “Experimental Tests of the Invisible Axion” 1983 PRL

## Slide 15
Pumped Cavity Mode
Magnet
antenna
Signal
TM010 Mode
Power buildup occurs when cavity resonance frequency is matched to axion mass.
Electric field strength enhanced by a factor of Q  105 at 1 GHz for copper cavity.

## Slide 16: Signal Power
Signal power:
Form Factor Cnl overlap of cavity mode
Dark Matter Density ρa
Axion Mass ma
Resonator Quality Factor QL
Axion velocity dispersion Qa
Couplings to Photon gγ ~ 0.97 for KSVZ model
gγ ~ 0.36 for DFSZ
TM010 mode
C010 ~ 0.69
TM011 mode
C011 ~ 0.0
B-field

## Slide 17: History
Pierre Sikivie, “Experimental Tests of the Invisible Axion”, PRL 1983
First and second generation haloscope experiments (1980s-90s) :
Cooled to 4 K w/FET transistor amplifiers, noise temperature range 3 - 20 K.
  BNL, University of Florida, Rochester/ Brookhaven/ Fermilab (RBF)
  ADMX- achieved KFVZ sensitivity
3rd generation (current):
Superconducting amplifiers <100 mK approaching standard quantum limit of noise.
  ADMX-G2. This talk
  Haystac– focus on higher frequencies than ADMX. Josephson Parametric Amplifiers, Squeezed states.
  CAPP. Korea Center for Axion and Precision Physics Research- ambitious program with several simultaneous searches planned.
Future: Bigger/ stronger magnets. More cavities, Beyond standard quantum noise limit?
Rochester-Brookhaven-Fermilab experiment, 1989

## Slide 18: ADMX Collaboration
Collaborating Institutions:
University of Washington
University of Florida
University of California, Berkeley
Washington University St. Louis
Sheffield University
Pacific Northwest National Lab
Lawrence Livermore National Lab
Los Alamos National Lab
National Radio Astronomy Observatory (NRAO)
Fermilab
The ADMX collaboration gratefully acknowledges support from the US Dept. of Energy, High Energy Physics DE-SC0011665 & DE-SC0010280 & DE-AC52-07NA27344
Also support from LLNL and PNNL LDRD programs and R&D support the Heising-Simons institute
18

## Slide 19
ADMX

## Slide 20
ADMX site: University of Washington
Center for Experimental Nuclear Physics and Astrophysics (CENPA)
Cleanroom
(with insert hanging)
Magnet in pit
Helium liquefier
DAQ & Controls

## Slide 21
Magnet: 8- Tesla Solenoid with 60 cm bore
Resonant Cavity with Tuning Rod

## Slide 22: Cryogenics
Mixing Chamber installed above ADMX Cavity
Significant cooling power required:
  Large cold mass in a magnetic field
  Friction in tuning rod system
  Electromechanical switches.
Dilution refrigerator (Janis Research) supplies 1 mW cooling at 100 mK.
Temperatures in 2016-2017 ranged from 150 mK (cavity) to 300 mK (electronics package)
Reduced temperatures in 2018 run.

## Slide 23: Tuning The Resonator
Tuning Rods
Frequency steps typically 1/10 cavity line width ~ 2 KHz

## Slide 24: Low Noise Electronics
To reach sensitivity of DFSZ axion models requires noise levels that were beyond state-of-the-art a few years ago.
Possible because of developments in Quantum Information Science community for applications such as Qubit readout:
  Microstrip Squid Amplifiers (Clarke group @ UC Berkeley)
  Josephson Parametric Amplifiers (Siddiqi group @ UC Berkeley).
  Traveling Wave Parametric Amplifiers (MIT Lincoln Labs). Wide instantaneous bandwidth.
Post amplification at 4 Kelvin using commercially available HFET technology.
Cold RF system needs capability for in-situ calibration and diagnostic functions.
Signal
Test Ports
Noise
calibration

## Slide 25: DC SQUID as an RF amplifier (MSA)
Principle of SQUIDs as microwave amplifiers
Very similar to conventional DC Squid.
Flux to voltage converter sensitive to a fraction of a flux quantum.
Adapted for high frequency use.
Supplied to ADMX by Clarke group at UC Berkeley.
Microstrip Squid Amplifier
Microstrip Squid Amplifier (MSA)
V
0
1
2
Φ
0
Φ
dV
dΦ
Nb coil, isolated from washer
(input)
Nb Counter electrode (output)
Nb washer (ground)
Nb-AlOx-Nb
junctions
Microstrip SQUID Amplifier (MSA):
Resistive shunts
Φ0 = h/2e  10-15 Tesla m2

## Slide 26: DC SQUID as an RF amplifier (MSA)
Principle of SQUIDs as microwave amplifiers
To couple a microwave signal into the SQUID:
  Cover the washer with an insulating layer (350nm of SiO2)
  Add a spiral path of conductor around central hole
  This creates a microstrip transmission line resonator between the input coil and SQUID washer.
GaAs varactor used to tune the microstrip resonator.
Microstrip Squid Amplifier
Microstrip Squid Amplifier (MSA)
MSA Varactor Tunability
Stripline Field Geometry

## Slide 27: Thermal Noise and Equivalent Noise Temperature
Thermal noise on a transmission line.
Density of modes on transmission line is . Each mode has energy kT.
Thermal noise power per frequency interval
Noise added by an amplifier is parametrized by an equivalent input noise temperature.
= T
“Detector”
Amplifier
Signal
Impedance Match
Temperature T
T
Thermal noise
Nyquist, 1928
L

## Slide 28: Standard Quantum Limit
When , cavity and transmission line modes need to be treated as quantum simple harmonic oscillator.
Two quantum effects each add ½ photon of noise per resolved cavity mode:
  Vacuum energy of simple harmonic oscillator is
  Phase insensitive linear amplifier with high gain must add an additional ( Haus- Caves theorem)
Minimum noise is 1 photon per mode. Standard Quantum Limit for noise temperature:
Energy Levels of a
harmonic oscillator
50 mK @ 1 GHz

## Slide 29: Noise Performance of Microstrip Squid Amplifiers
Achieved TN= 48 mK at 600 MHz during testing at UC Berkeley
1.7 x quantum limit.
In ADMX operation, system noise temperatures has additional contributions from:
  Black body radiation in cavity
  Attenuation
  Post amplification stages

## Slide 30
MSA Operation in ADMX 2017/ 2018 Runs
Amplifier package at higher temperature than resonator due to thermal short.
Causes distinctive “dip” in noise power at cavity resonance.
Typical system noise temperature was 500 mK.
Notes: Two sources of asymmetry in the signal.
Interference off reflected power of the cavity (off resonance)
Standing wave effects from reflection off the unknown MSA input impedance
Asymmetric because it relies on the complex impedance of the resonator/antenna.
Near resonance it has a positive imaginary part on one side and a negative imaginary part of the other so the interference effects are different on each side.
Different colors are different MSA gain bias (red is highest gain)

## Slide 31: Signal to Noise Ratio- Example
Suppose we have
Bandwidth of axion is due to halo velocity dispersion
 1 kHz at 1 GHz axion frequency
So
Still about three orders of magnitude larger than the signal!

## Slide 32
Noise reduction by averaging

## Slide 33: Operating Procedure
The cavity frequency is scanned over a region until the desired SNR is achieved.
Convolution with filter matched to expected axion line shape.
Typically we have ~106 independent measurements on each axion linewidth, averaged to reduce noise by
We then examine the combined power spectrum for signs of excess
Excess power regions can be statistical fluctuations, synthetically injected signals, RF interference, or axions
Excess power regions are rescanned to see if they persist
Persistent candidates are subjected to a variety of confirmation tests: for example: magnet field changes or probing with other cavity modes.
We do blind signal injection, so we always have candidates

## Slide 34: Predicted Axion Signal Shape
Recent N-Body models actually suggest the axion lineshape is narrower than the standard virialized model.
Our analysis searches for both.
Lineshape scaled to current ADMX run
Adapted from: Lentz et al. Ap.J. 845 (2017)

## Slide 35: You might have an axion if the signal…
Can’t be seen in the room outside of the magnetic field
Persists all the time
Follows the Lorentzian lineshape of the cavity
Is suppressed in non TM010 modes
Was not a synthetic axion signal injected by the calibration team
Scales with the B2 of the magnet
Has an annual frequency modulation
No candidates passed tests in 2017 run.

## Slide 36: First ADMX-G2 Result (Data from 2017 Run)
ArXiv 1804.05750 & PRL April 2018
Exclude DFSZ models at 90% CL from 2.66-2.82 meV.

## Slide 37: ADMX 2018 Run- Results Coming Soon
Continued DFSZ sensitivity scan in the 680 to 800 MHz range.
Lower physical and noise temperature due to cryogenic improvements.
  Tnoise -> 350 mK
Scan speed increase by factor of two with higher signal to noise ratio.
Stay tuned for results – paper mid 2019.
2017
Excluded
2018
In Progress

## Slide 38: How to Speed up Axion Searches
Scan Rate Vs Frequency & other parameters
Lower Noise Amplifiers
Stronger Magnet
More Detector Volume:
Array of
Resonators
Effective scan rate of ADMX in 2018 was  1 MHz/ day
As we move up in frequency,
    Expected axion coupling increases
    Cavity volume decreases, decreasing signal
    Cavity Q decreases, decreasing signal
    Quantum limit increases, increasing noise
Higher Q:
Superconducting or Dielectric Resonators

## Slide 39: Quantum Sensor R&D for Axion Detection
Axion detection is natural application for quantum sensors.
  Current Microstrip Squid Amplifiers (MSAs) and Josephson Parametric Amplifiers (JPAs) with noise close to standard quantum limit.
  Future: Squeezed states prepared by JPAs, Qubit photon counters.
Aluminum qubit on a sapphire substrate in a copper resonant cavity. A single photon in the cavity produces a qubit frequency shift (Dave Schuster, Akash Dixit, Aaron Chou)
JPAs used for ADMX-G2
I. Siddiqi, UC Berkeley
Qubit sensitivity to Axions (A. Chou, FNAL)

## Slide 40
ADMX Cavities up to 4 GHz
2020-2021
4-Cavity Array
8 piezoelectric actuators
1500-2300 MHz
2022-2024
14-Cavity array
2.3- 4 GHz
2019-2020
800-1500 MHz
Large tuning rod
Used in 2016-2018 Runs
580-890 MHz

## Slide 41: R&D Towards High Frequency (>4 GHz) Resonators
Challenging to fill a large volume with small tunable structures (“Swiss Watch” problem)
Number of elements goes as
Explore systems that allow simultaneous tuning of many elements with only a few mechanical motions.
  Photonic bandgap cavity
  “Comb Cavity”
  Electronic fine tuning using nonlinear dielectrics
Comb cavity (FNAL)
Array of posts (LLNL)
“Pizza” Cavity (U. Florida)

## Slide 42
Current System for Turning Tuning Rods (~1996-2019)
Driven by stepper motors at room temperature.
19,600:1 gear reduction allows for very small tuning rod motions with high torque.
Not suitable for large numbers of cavities.

## Slide 43: Cryogenic Piezoelectric Actuators for Cavity Tuning
Use commercial miniature cryogenic rotary and linear piezoelectric actuators (Attocube)
“Sidecar” 4-6 GHz Cavity
Linear Piezo drive controls antenna depth
Rotary Piezo connected to tuning Rod

## Slide 44: Sidecar cavity results 2018
Proof of principle for piezoelectrically tuned cavities.
New exclusion limits at 17, 22, and 30 ueV
High noise temperature (7 Kelvin)– HFET amplifiers.
PRL, January 2019

## Slide 45
Assembly of 800-1500 MHz Hardware in February 2019
800-1500 MHz Resonator
Improved cryogenic electronics package– goals is to bring electronics temperature below 100 mK & achieve factor of 4 speedup in data taking.
Next run will start in April.

## Slide 46: Timeline For Current and Next Generation Experiments
ADMX- G2 Approved for operation through 2021 at University of Washington, with coverage up to 2 GHz.
We hope to extend running at U Washington to 2024 (4 GHz).
Next generation experiment with a higher field magnet could start as early as 2022.

## Slide 47: Summary
ADMX achieved sensitivity to DFSZ axion models, a long standing goal of the field.
Improved sensitivity in current generation of experiments due to lower temperatures and better amplifiers.
Noise temperature reduction and other optimizations will increase scan speed over time.
Exciting times-- a definitive test of most interesting QCD axion dark matter models is possible.

## Slide 48: Extra Slides

## Slide 49: ADMX Collaboration
Collaborating Institutions:
University of Washington
University of Florida
University of California, Berkeley
Washington University St. Louis
Sheffield University
Pacific Northwest National Lab
Lawrence Livermore National Lab
Los Alamos National Lab
National Radio Astronomy Observatory (NRAO)
Fermilab
The ADMX collaboration gratefully acknowledges support from the US Dept. of Energy, High Energy Physics DE-SC0011665 & DE-SC0010280 & DE-AC52-07NA27344
Also support from LLNL and PNNL LDRD programs and R&D support the Heising-Simons institute
49

## Slide 50: Quantum Limit
signal photon rate
*single photon of noise
per resolved mode

## Slide 51: Josephson Junction
Flux Quantization
 = n0 (n = 0, ±1, ±2, ...)
Φ0 = h/2e
In presence of Josephson element the quantization condition becomes:
 - (δ/2π) 0 = n0
F = nF0
J
Josephson Tunneling
I
superconductor
superconductor
~ 20 Å
insulating
barrier
I
Superconducting state has macroscopic wavefunction.
I and V across the junction are given by the Josephson relations:
= sin V=/2π
SQUIDs as microwave amplifiers
Courtesy: Sean O’Kelley, UC Berkeley

## Slide 52: Josephson Parametric amplifier (JPA)
wpump
wsignal
widler
wpump
wsignal
JPA
Nonlinear LJ
modulated
two normal modes
of swing:
signal + idler
Parametric amplifier: Oscillator whose resonance frequency is modulated
Oscillating system a λ/4 resonator
Inductance varied with SQUID (flux dependent nonlinear inductor)
Energy transfer from pump to
two normal modes of swing
Noise – Quantum Limit
Paramp schematic: L. Zhong et al., “Squeezing with a fluxdriven Josephson parametric amplifier,” New J. Phys. 15, 125013 (2013).

## Slide 53: Current data run: JPA operations
2 mm
Josephson Parameteric Amplifier (JPA) provided by Siddiq Group at UC Berkeley
Current JPA band: 685 MHz – 800 MHz  limited by circulators.
2nd Channel is an MSA tunable from 800 – 890 MHz
Two amplifiers with complementary tuning ranges!
Minimize number of experimental insertions
Redundancy
As we continue up in frequency we will transition to using entirely JPAs (shown to work up to > 10 GHz)
Prof. Irfan Siddiqi: UC Berkeley

## Slide 54
Fermilab Initiatives to Surpass The “Standard Quantum Limit”
Fascinating new direction in detector technology well supported by DOE and other agencies
New collaborations with quantum information groups at Chicago, NIST

## Slide 55: Beyond the Quantum Limit
Quantum limit comes from trying to measure both amplitude and phase of a harmonic oscillator (mode of E field)
Can we avoid measuring both amplitude and phase?
Various proposals
  “Squeezing the vacuum” using Josephson Parametric Amplifiers (Haystac)
  Qubit single microwave photon detectors (R&D at Lawrence Livermore National Lab and Fermilab)
  Single microwave photon counting using Rydberg atoms (R&D at Yale)
Qubit (FNAL/ Chicago)

## Slide 56
Akash Dixit

## Slide 57
ADMX: Collaboration
Sponsors
ADMX now DOE Gen 2 project
Primary sponsor
*
R&D support
Notes: Look at the # of institutions (10) and # of scientist, students (look at the latest MOUs). Count engineers/technicians?
LLNL: 2 scientists / 1 student / 1 technician
LANL: 1: 1 scientist
WU: 3 scientists / 1 student
UFL: 3 scientists / 3 students / 1 engineer
UW: 4 scientists / 3 students
NRAO: 1 scientist
FNAL: 5 scientists, 1 student,
Sheffield:1 scientist
UCB: 4: 2 scientists & 2 students
PNNL: 3 scientists & 2 engineers
Total of ~ 40 people (scientists, postdocs, students and engineers)

## Slide 58: The QCD Axion- A Very Predictive Model
Everything depends on just one unknown parameter– the axion decay constant fa
  The axion mass.
  Coupling to gluons and photons.
  The cosmological abundance*
 fA
*Vacuum realignment contribution for post inflation scenario, not including cosmic strings & domain walls…

## Slide 59: Axion Mass
QCD effects at the time of the QCD phase transition (quark- gluon plasma -> free particles) cause a small tilt in the Peccei Quinn potential producing an axion mass.
Axion mass is determined by curvature of potential around minimum.
 fA

## Slide 60: CP Violation in QCD
R.D. Peccei, Hep-ph/0607268
The QCD Lagrangian contains a term that changes sign under Parity or Time reversal
Strong coupling constant
Gluon field strengths
Limits on the neutron electric dipole moment (< 3 x 10-26 e cm) constrain the CP violation parameter Q<10-9

## Slide 61
Graham, Irastrorza, Lamoreaux, Linder and Van Bibber, arXiv:1602.00039
Axion 2d Sensitivity Plot: Photon Coupling vs Mass
Constructed to resemble standard WIMP sensitivity plot.
Allows for a more general parameter space of “axion like particles” or ALPS with independent mass & cross section.
QCD axion appears along diagonal band.
gagg
a

## Slide 62: Production of Dark Matter by Vacuum Realignment
After PQ symmetry breaking the  angle is a random number.
Tilting of PQ potential below QCD phase transition causes the field to roll to its minimum, converting vacuum energy to axion particles.
Axion dark matter density today determined by random initial value of .
Can assume different values in causally disconnected regions of space-> domain walls.
0.37
1.12
2.01
0.63
3.14
1.93
0.01
1.57
0.17
Cosmic axion
string
Random

## Slide 63: Beyond the Quantum Limit
Quantum limit comes from trying to measure both amplitude and phase of a harmonic oscillator (mode of E field)
Can we avoid measuring both amplitude and phase?
Various proposals
  “Squeezing the vacuum” using Josephson Parametric Amplifiers (Haystac)
  Qubit single microwave photon detectors
  Single microwave photon counting using Rydberg atoms.